## Slide 1: Assembly Language for x86 Processors
Copyright © 2020, 2015, 2011 Pearson Education, Inc. All Rights Reserved
Conditional Processing
Chapter 6
Eighth Edition

## Slide 2: Chapter Overview
Boolean and Comparison Instructions
Conditional Jumps
Conditional Loop Instructions
Conditional Structures
Application: Finite-State Machines
Conditional Control Flow Directives

## Slide 3: Boolean and Comparison Instructions
CPU Status Flags
AND Instruction
OR Instruction
XOR Instruction
NOT Instruction
Applications
TEST Instruction
CMP Instruction

## Slide 4: Status Flags – Review (1 of 2)
The Zero flag is set when the result of an operation equals zero.
The Carry flag is set when an instruction generates a result that is too large (or too small) for the destination operand.
The Sign flag is set if the destination operand is negative, and it is clear if the destination operand is positive.

## Slide 5: Status Flags – Review (2 of 2)
The Overflow flag is set when an instruction generates an invalid signed result (bit 7 carry is XORed with bit 6 Carry).
The Parity flag is set when an instruction generates an even number of 1 bits in the low byte of the destination operand.
The Auxiliary Carry flag is set when an operation produces a carry out from bit 3 to bit 4

## Slide 6: AND Instruction
AND
Performs a Boolean AND operation between each pair of matching bits in two operands
Syntax:
AND destination, source
(same operand types as MOV)

## Slide 7: OR Instruction
OR
Performs a Boolean OR operation between each pair of matching bits in two operands
Syntax:
OR destination, source

## Slide 8: XOR Instruction
XOR is a useful way to toggle (invert) the bits in an operand.
XOR
Performs a Boolean exclusive-OR operation between each pair of matching bits in two operands
Syntax:
XOR destination, source

## Slide 9: NOT Instruction
NOT
Performs a Boolean NOT operation on a single destination operand
Syntax:
NOT destination

## Slide 10: Bit-Mapped Sets
Binary bits indicate set membership
Efficient use of storage
Also known as bit vectors

## Slide 11: Bit-Mapped Set Operations
Set Complement
mov eax,SetX
not eax
Set Intersection
mov eax,setX
and eax,setY
Set Union
mov eax,setX
or eax,setY

## Slide 12: Applications (1 of 5)
mov al,'a' ; AL = 01100001b
and al,11011111b ; AL = 01000001b
Task: Convert the character in AL to upper case.
Solution: Use the AND instruction to clear bit 5.

## Slide 13: Applications (2 of 5)
The ASCII digit '6' = 00110110b
mov al,6 ; AL = 00000110b
or al,00110000b ; AL = 00110110b
Task: Convert a binary decimal byte into its equivalent ASCII decimal digit.
Solution: Use the OR instruction to set bits 4 and 5.

## Slide 14: Applications (3 of 5)
This code only runs in Real-address mode, and it does not work under Windows NT, 2000, or XP.
mov ax,40h ; BIOS segment
mov ds,ax
mov bx,17h ; keyboard flag byte
or BYTE PTR [bx],01000000b ; CapsLock on
Task: Turn on the keyboard CapsLock key
Solution: Use the OR instruction to set bit 6 in the keyboard flag byte at 0040:0017h in the BIOS data area.

## Slide 15: Applications (4 of 5)
Your turn: Write code that jumps to a label if an integer is negative.
JZ (jump if Zero) is covered in Section 6.3.
mov ax,wordVal
and ax,1 ; low bit set?
jz EvenValue ; jump if Zero flag set
Task: Jump to a label if an integer is even.
Solution: AND the lowest bit with a 1. If the result is Zero, the number was even.

## Slide 16: Application (5 of 5)
ORing any number with itself does not change its value.
or al,al
jnz IsNotZero ; jump if not zero
Task: Jump to a label if the value in AL is not zero.
Solution: OR the byte with itself, then use the JNZ (jump if not zero) instruction.

## Slide 17: TEST Instruction (1 of 2)
test al,00000011b
jnz ValueFound
Performs a nondestructive AND operation between each pair of matching bits in two operands
No operands are modified, but the Zero flag is affected.
Example: jump to a label if either bit 0 or bit 1 in AL is set.

## Slide 18: TEST Instruction (2 of 2)
test al,00000011b
jz ValueNotFound
Example: jump to a label if neither bit 0 nor bit 1 in AL is set.

## Slide 19: CMP Instruction (1 of 3)
mov al,4
cmp al,5 ; Carry flag set
Example: destination < source
mov al,5
cmp al,5 ; Zero flag set
Compares the destination operand to the source operand
  Nondestructive subtraction of source from destination (destination operand is not changed)
Syntax: CMP destination, source
Example: destination == source

## Slide 20: CMP Instruction (2 of 3)
(both the Zero and Carry flags are clear)
mov al,6
cmp al,5 ; ZF = 0, CF = 0
Example: destination > source

## Slide 21: CMP Instruction (3 of 3)
mov al,-1
cmp al,5 ; Sign flag != Overflow flag
Example: destination < source
mov al,5
cmp al,-2 ; Sign flag == Overflow flag
Example: destination > source
The comparisons shown here are performed with signed integers.

## Slide 22: Boolean Instructions in 64-Bit Mode
64-bit boolean instructions, for the most part, work the same as 32-bit instructions
If the source operand is a constant whose size is less than 32 bits and the destination is the lower part of a 64-bit register or memory operand, all bits in the destination operand are affected
When the source is a 32-bit constant or register, only the lower 32 bits of the destination operand are affected

## Slide 23: What's Next (1 of 5)
Boolean and Comparison Instructions
Conditional Jumps
Conditional Loop Instructions
Conditional Structures
Application: Finite-State Machines
Conditional Control Flow Directives

## Slide 24: Conditional Jumps
Jumps Based On . . .
  Specific flags
  Equality
  Unsigned comparisons
  Signed Comparisons
Applications
Encrypting a String
Bit Test (BT) Instruction

## Slide 25: Jcond Instruction
A conditional jump instruction branches to a label when specific register or flag conditions are met
Specific jumps:
  JB, JC - jump to a label if the Carry flag is set
  JE, JZ - jump to a label if the Zero flag is set
  JS - jump to a label if the Sign flag is set
  JNE, JNZ - jump to a label if the Zero flag is clear
  JECXZ - jump to a label if ECX = 0

## Slide 26: Jcond Ranges
Prior to the 386:
  jump must be within –128 to +127 bytes from current location counter
x86 processors:
  32-bit offset permits jump anywhere in memory

## Slide 27: Jumps Based on Specific Flags

## Slide 28: Jumps Based on Equality

## Slide 29: Jumps Based on Unsigned Comparisons

## Slide 30: Jumps Based on Signed Comparisons

## Slide 31: Applications (1 of 4)
cmp eax,ebx
jg Greater
Task: Jump to a label if signed EAX is greater than EBX
Solution: Use CMP, followed by JG
cmp eax,ebx
ja Larger
Task: Jump to a label if unsigned EAX is greater than EBX
Solution: Use CMP, followed by JA

## Slide 32: Applications (2 of 4)
cmp eax,Val1
jle L1
Jump to label L1 if signed EAX is less than or equal to Val1
cmp eax,Val1
jbe L1 ; below or equal
Jump to label L1 if unsigned EAX is less than or equal to Val1

## Slide 33: Applications (3 of 4)
  mov Small,ax
  cmp bx,ax
  jnl Next
  mov Small,bx
Next:
Compare signed AX to BX, and copy the smaller of the two into a variable named Small
  mov Large,bx
  cmp ax,bx
  jna Next
  mov Large,ax
Next:
Compare unsigned AX to BX, and copy the larger of the two into a variable named Large

## Slide 34: Applications (4 of 4)
test DWORD PTR [edi],1
jz L2
Jump to label L2 if the doubleword in memory pointed to by EDI is even
  cmp WORD PTR [esi],0
  je L1
Jump to label L1 if the memory word pointed to by ESI equals Zero

## Slide 35: Applications
and al,00001011b ; clear unwanted bits
cmp al,00001011b ; check remaining bits
je L1 ; all set? jump to L1
Task: Jump to label L1 if bits 0, 1, and 3 in AL are all set.
Solution: Clear all bits except bits 0, 1,and 3. Then compare the result with 00001011 binary.

## Slide 36: Your Turn . . . (1 of 8)
Write code that jumps to label L1 if either bit 4, 5, or 6 is set in the BL register.
Write code that jumps to label L1 if bits 4, 5, and 6 are all set in the BL register.
Write code that jumps to label L2 if AL has even parity.
Write code that jumps to label L3 if EAX is negative.
Write code that jumps to label L4 if the expression (EBX – ECX) is greater than zero.

## Slide 37: Encrypting a String
KEY = 239 ; can be any byte value
BUFMAX = 128
.data
buffer BYTE BUFMAX+1 DUP(0)
bufSize DWORD BUFMAX
.code
  mov ecx,bufSize ; loop counter
  mov esi,0 ; index 0 in buffer
L1:
  xor buffer[esi],KEY ; translate a byte
  inc esi ; point to next byte
  loop L1
The following loop uses the XOR instruction to transform every character in a string into a new value.

## Slide 38: String Encryption Program
Enter the plain text: Attack at dawn.
Cipher text: «¢¢Äîä-Ä¢-ïÄÿü-Gs
Decrypted: Attack at dawn.
View the Encrypt.asm program's source code. Sample output:
Tasks:
  Input a message (string) from the user
  Encrypt the message
  Display the encrypted message
  Decrypt the message
  Display the decrypted message

## Slide 39: BT (Bit Test) Instruction
bt AX,9 ; CF = bit 9
jc L1 ; jump if Carry
Copies bit n from an operand into the Carry flag
Syntax: BT bitBase, n
  bitBase may be r/m16 or r/m32
  n may be r16, r32, or imm8
Example: jump to label L1 if bit 9 is set in the AX register:

## Slide 40: What's Next (2 of 5)
Boolean and Comparison Instructions
Conditional Jumps
Conditional Loop Instructions
Conditional Structures
Application: Finite-State Machines
Conditional Control Flow Directives

## Slide 41: Conditional Loop Instructions
LOOPZ and LOOPE
LOOPNZ and LOOPNE

## Slide 42: LOOPZ and LOOPE
In 32-bit mode, ECX is the loop counter register. In 16-bit real-address mode, CX is the counter, and in 64-bit mode, RCX is the counter.
Syntax:
  LOOPE destination
  LOOPZ destination
Logic:
  ECX  ECX – 1
  if ECX > 0 and ZF=1, jump to destination
Useful when scanning an array for the first element that does not match a given value.

## Slide 43: LOOPNZ and LOOPNE
LOOPNZ (LOOPNE) is a conditional loop instruction
Syntax:
  LOOPNZ destination
  LOOPNE destination
Logic:
  ECX  ECX – 1;
  if ECX > 0 and ZF=0, jump to destination
Useful when scanning an array for the first element that matches a given value.

## Slide 44: LOOPNZ Example
.data
array SWORD -3,-6,-1,-10,10,30,40,4
sentinel SWORD 0
.code
  mov esi,OFFSET array
  mov ecx,LENGTHOF array
next:
  test WORD PTR [esi],8000h ; test sign bit
  pushfd ; push flags on stack
  add esi,TYPE array
  popfd ; pop flags from stack
  loopnz next ; continue loop
  jnz quit ; none found
  sub esi,TYPE array ; ESI points to value
quit:
The following code finds the first positive value in an array:

## Slide 45: Your Turn . . . (2 of 8)
.data
array SWORD 50 DUP(?)
sentinel SWORD 0FFFFh
.code
  mov esi,OFFSET array
  mov ecx,LENGTHOF array
L1: cmp WORD PTR [esi],0 ; check for zero
(fill in your code here)
quit:
Locate the first nonzero value in the array. If none is found, let ESI point to the sentinel value:

## Slide 46: . . . (solution)
.data
array SWORD 50 DUP(?)
sentinel SWORD 0FFFFh
.code
  mov esi,OFFSET array
  mov ecx,LENGTHOF array
L1: cmp WORD PTR [esi],0 ; check for zero
  pushfd ; push flags on stack
  add esi,TYPE array
  popfd ; pop flags from stack
  loope L1 ; continue loop
  jz quit ; none found
  sub esi,TYPE array ; ESI points to value
quit:

## Slide 47: What's Next (3 of 5)
Boolean and Comparison Instructions
Conditional Jumps
Conditional Loop Instructions
Conditional Structures
Application: Finite-State Machines
Conditional Control Flow Directives

## Slide 48: Conditional Structures
Block-Structured IF Statements
Compound Expressions with AND
Compound Expressions with OR
WHILE Loops
Table-Driven Selection

## Slide 49: Block-Structured IF Statements
  mov eax,op1
  cmp eax,op2
  jne L1
  mov X,1
  jmp L2
L1: mov X,2
L2:
if( op1 == op2 )
X = 1;
else
X = 2;
Assembly language programmers can easily translate logical statements written in C++/Java into assembly language. For example:

## Slide 50: Your Turn . . . (3 of 8)
(There are multiple correct solutions to this problem.)
  cmp ebx,ecx
  ja next
  mov eax,5
  mov edx,6
next:
if( ebx <= ecx )
{
eax = 5;
edx = 6;
}
Implement the following pseudocode in assembly language. All values are unsigned:

## Slide 51: Your Turn . . . (4 of 8)
(There are multiple correct solutions to this problem.)
  mov eax,var1
  cmp eax,var2
  jle L1
  mov var3,6
  mov var4,7
  jmp L2
L1: mov var3,10
L2:
if( var1 <= var2 )
var3 = 10;
else
{
var3 = 6;
var4 = 7;
}
Implement the following pseudocode in assembly language. All values are 32-bit signed integers:

## Slide 52: Compound Expression with AND (1 of 3)
if (al > bl) AND (bl > cl)
X = 1;
When implementing the logical AND operator, consider that HLLs use short-circuit evaluation
In the following example, if the first expression is false, the second expression is skipped:

## Slide 53: Compound Expression with AND (2 of 3)
cmp al,bl ; first expression...
ja L1
jmp next
L1:
cmp bl,cl ; second expression...
ja L2
jmp next
L2: ; both are true
mov X,1 ; set X to 1
next:
This is one possible implementation . . .
if (al > bl) AND (bl > cl)
X = 1;

## Slide 54: Compound Expression with AND (3 of 3)
cmp al,bl ; first expression...
jbe next ; quit if false
cmp bl,cl ; second expression...
jbe next ; quit if false
mov X,1 ; both are true
next:
But the following implementation uses 29% less code by reversing the first relational operator. We allow the program to "fall through" to the second expression:
if (al > bl) AND (bl > cl)
X = 1;

## Slide 55: Your Turn . . . (5 of 8)
  cmp ebx,ecx
  ja next
  cmp ecx,edx
  jbe next
  mov eax,5
  mov edx,6
next:
if( ebx <= ecx
&& ecx > edx )
{
eax = 5;
edx = 6;
}
Implement the following pseudocode in assembly language. All values are unsigned:

## Slide 56: Compound Expression with OR (1 of 2)
if (al > bl) OR (bl > cl)
X = 1;
When implementing the logical OR operator, consider that HLLs use short-circuit evaluation
In the following example, if the first expression is true, the second expression is skipped:

## Slide 57: Compound Expression with OR (2 of 2)
cmp al,bl ; is AL > BL?
ja L1 ; yes
cmp bl,cl ; no: is BL > CL?
jbe next ; no: skip next statement
L1: mov X,1 ; set X to 1
next:
We can use "fall-through" logic to keep the code as short as possible:
if (al > bl) OR (bl > cl)
X = 1;

## Slide 58: WHILE Loops
top: cmp eax,ebx ; check loop condition
jae next ; false? exit loop
inc eax ; body of loop
jmp top ; repeat the loop
next:
This is a possible implementation:
while( eax < ebx)
eax = eax + 1;
A WHILE loop is really an IF statement followed by the body of the loop, followed by an unconditional jump to the top of the loop. Consider the following example:

## Slide 59: Your Turn . . . (6 of 8)
top: cmp ebx,val1 ; check loop condition
ja next ; false? exit loop
add ebx,5 ; body of loop
dec val1
jmp top ; repeat the loop
next:
while( ebx <= val1)
{
ebx = ebx + 5;
val1 = val1 - 1
}
Implement the following loop, using unsigned 32-bit integers:

## Slide 60: Table-Driven Selection (1 of 4)
Table-driven selection uses a table lookup to replace a multiway selection structure
Create a table containing lookup values and the offsets of labels or procedures
Use a loop to search the table
Suited to a large number of comparisons

## Slide 61: Table-Driven Selection (2 of 4)
.data
CaseTable BYTE 'A' ; lookup value
DWORD Process_A ; address of procedure
EntrySize = ($ - CaseTable)
BYTE 'B'
DWORD Process_B
BYTE 'C'
DWORD Process_C
BYTE 'D'
DWORD Process_D
NumberOfEntries = ($ - CaseTable) / EntrySize
Step 1: create a table containing lookup values and procedure offsets:

## Slide 62: Table-Driven Selection (3 of 4)
Table of Procedure Offsets:

## Slide 63: Table-Driven Selection (4 of 4)
required for procedure pointers
mov ebx,OFFSET CaseTable ; point EBX to the table
mov ecx,NumberOfEntries ; loop counter
L1: cmp al,[ebx] ; match found?
jne L2 ; no: continue
call NEAR PTR [ebx + 1] ; yes: call the procedure
call WriteString ; display message
call Crlf
jmp L3 ; and exit the loop
L2: add ebx,EntrySize ; point to next entry
loop L1 ; repeat until ECX = 0
L3:
Step 2: Use a loop to search the table. When a match is found, call the procedure offset stored in the current table entry:

## Slide 64: What's Next (4 of 5)
Boolean and Comparison Instructions
Conditional Jumps
Conditional Loop Instructions
Conditional Structures
Application: Finite-State Machines
Conditional Control Flow Directives

## Slide 65: Application: Finite-State Machines (1 of 2)
A finite-state machine (FSM) is a graph structure that changes state based on some input. Also called a state-transition diagram.
We use a graph to represent an FSM, with squares or circles called nodes, and lines with arrows between the circles called edges.

## Slide 66: Application: Finite-State Machines (2 of 2)
A FSM is a specific instance of a more general structure called a directed graph.
Three basic states, represented by nodes:
  Start state
  Terminal state(s)
  Nonterminal state(s)

## Slide 67: Finite-State Machine
Accepts any sequence of symbols that puts it into an accepting (final) state
Can be used to recognize, or validate a sequence of characters that is governed by language rules (called a regular expression)
Advantages:
  Provides visual tracking of program's flow of control
  Easy to modify
  Easily implemented in assembly language

## Slide 68: Finite-State Machine Examples
FSM that recognizes signed integers:
FSM that recognizes strings beginning with 'x', followed by letters 'a'..'y', ending with 'z':

## Slide 69: Your Turn . . . (7 of 8)
Explain why the following FSM does not work as well for signed integers as the one shown on the previous slide:

## Slide 70: Implementing an FSM
View the Finite.asm source code.
StateA:
call Getnext ; read next char into AL
cmp al,'+' ; leading + sign?
je StateB ; go to State B
cmp al,'-' ; leading - sign?
je StateB ; go to State B
call IsDigit ; ZF = 1 if AL = digit
jz StateC ; go to State C
call DisplayErrorMsg ; invalid input found
jmp Quit
The following is code from State A in the Integer FSM:

## Slide 71: IsDigit Procedure
IsDigit PROC
cmp al,'0' ; ZF = 0
jb ID1
cmp al,'9' ; ZF = 0
ja ID1
test ax,0 ; ZF = 1
ID1: ret
IsDigit ENDP
Receives a character in AL. Sets the Zero flag if the character is a decimal digit.

## Slide 72: Flowchart of State A
State A accepts a plus or minus sign, or a decimal digit.

## Slide 73: Your Turn . . . (8 of 8)
Draw a FSM diagram for hexadecimal integer constant that conforms to MASM syntax.
Draw a flowchart for one of the states in your FSM.
Implement your FSM in assembly language. Let the user input a hexadecimal constant from the keyboard.

## Slide 74: What's Next (5 of 5)
Boolean and Comparison Instructions
Conditional Jumps
Conditional Loop Instructions
Conditional Structures
Application: Finite-State Machines
Conditional Control Flow Directives

## Slide 75: Creating IF Statements
Runtime Expressions
Relational and Logical Operators
MASM-Generated Code
.REPEAT Directive
.WHILE Directive

## Slide 76: Runtime Expressions
MASM generates "hidden" code for you, consisting of code labels, CMP and conditional jump instructions.
.IF eax > ebx && eax > ecx
mov edx,1
.ELSE
mov edx,2
.ENDIF
.IF eax > ebx
mov edx,1
.ELSE
mov edx,2
.ENDIF
.IF, .ELSE, .ELSEIF, and .ENDIF can be used to evaluate runtime expressions and create block-structured IF statements.
Examples:

## Slide 77: Relational and Logical Operators

## Slide 78: Signed and Unsigned Comparisons (1 of 4)
MASM automatically generates an unsigned jump (JBE) because val1 is unsigned.
mov eax,6
cmp eax,val1
jbe @C0001
mov result,1
@C0001:
Generated code:
.data
val1 DWORD 5
result DWORD ?
.code
mov eax,6
.IF eax > val1
mov result,1
.ENDIF

## Slide 79: Signed and Unsigned Comparisons (2 of 4)
MASM automatically generates a signed jump (JLE) because val1 is signed.
mov eax,6
cmp eax,val1
jle @C0001
mov result,1
@C0001:
Generated code:
.data
val1 SDWORD 5
result SDWORD ?
.code
mov eax,6
.IF eax > val1
mov result,1
.ENDIF

## Slide 80: Signed and Unsigned Comparisons (3 of 4)
MASM automatically generates an unsigned jump (JBE) when both operands are registers . . .
mov ebx,5
mov eax,6
cmp eax,ebx
jbe @C0001
mov result,1
@C0001:
Generated code:
.data
result DWORD ?
.code
mov ebx,5
mov eax,6
.IF eax > ebx
mov result,1
.ENDIF

## Slide 81: Signed and Unsigned Comparisons (4 of 4)
. . . unless you prefix one of the register operands with the SDWORD PTR operator. Then a signed jump is generated.
mov ebx,5
mov eax,6
cmp eax,ebx
jle @C0001
mov result,1
@C0001:
Generated code:
.data
result SDWORD ?
.code
mov ebx,5
mov eax,6
.IF SDWORD PTR eax > ebx
mov result,1
.ENDIF

## Slide 82: .REPEAT Directive
; Display integers 1 – 10:
mov eax,0
.REPEAT
inc eax
call WriteDec
call Crlf
.UNTIL eax == 10
Executes the loop body before testing the loop condition associated with the .UNTIL directive.
Example:

## Slide 83: .WHILE Directive
; Display integers 1 – 10:
mov eax,0
.WHILE eax < 10
inc eax
call WriteDec
call Crlf
.ENDW
Tests the loop condition before executing the loop body The .ENDW directive marks the end of the loop.
Example:

## Slide 84: Summary (1 of 2)
Bitwise instructions (AND, OR, XOR, NOT, TEST)
  manipulate individual bits in operands
CMP – compares operands using implied subtraction
  sets condition flags

## Slide 85: Summary (2 of 2)
Conditional Jumps & Loops
  equality: JE, JNE
  flag values: JC, JZ, JNC, JP, ...
  signed: JG, JL, JNG, ...
  unsigned: JA, JB, JNA, ...
  LOOPZ, LOOPNZ, LOOPE, LOOPNE
Flowcharts – logic diagramming tool
Finite-state machine – tracks state changes at runtime

## Slide 86: 4C 6F 70 70 75 75 6E

## Slide 87: Copyright
This work is protected by United States copyright laws and is provided solely for the use of instructors in teaching their courses and assessing student learning. Dissemination or sale of any part of this work (including on the World Wide Web) will destroy the integrity of the work and is not permitted. The work and materials from it should never be made available to students except by instructors using the accompanying text in their classes. All recipients of this work are expected to abide by these restrictions and to honor the intended pedagogical purposes and the needs of other instructors who rely on these materials.
Notes: If this slide was not included in the original PPT, it should be added.